## Slide 1: Calculating a Series Circuit

## Slide 2: Find the voltage , current ,power and total resistance

## Slide 3: For this exercise we need to know the formula

## Slide 4: If we know all the resistances, simply add them up

## Slide 5: We add all of them up to get=1100 ohm

## Slide 6: Keep in mind..
In a series circuit, the one thing that is common is that the total current travels throughout the entire circuit… so knowing this, we have 1100 ohm and a voltage of 120..
The calculation for calculating current is
I for current is E/R which is approx
.1091 Amp

## Slide 7: Now that we have total current and voltage, we can calculate the total Power. The formula is P= I times E or .1091 times 120= 13.091 W

## Slide 8: Keep in mind
In a series circuit even though the current is the same throughout, the voltage is not.. Its only at the souce however once it travels through the circuit, it drops a bit at each resistor.. Keep in mind that the total voltage drop will add up to the total voltage. So using ohms law, we use the E or Voltage ( E stands for electromotive force) to calculate .

## Slide 9: R1 is 110 ohm and we know the Current to be .1091A therefore if E is I X R the result for R1 is 12.001 V

## Slide 10: We can now calculate the power since we now know at least 2 values

## Slide 11: Continue with the rest of the resistors and calculate the voltage drops at each resistor, and wattage at each resistor and your answers are????

## Slide 12: Answer sheet..