## Slide 1: How to calculate an off grid system
sample

## Slide 2: For the 120 volt loads
Add up all the wattage keep that aside, that will be the min. needed for the inverter size..
See how much time the items will be running for.
If you don’t know the amperage? Figure it out using ohms law.
If an item is 8.3 amp for one hr, then use 8.3 AH
If 8.3 amp for 2 hrs? then its 16.6 AH
Add up all the 120 volt AH and keep that aside

## Slide 3: Calculating AH from the battery
From your 120 volt calculation, take the sum of the AH , that will be the AH usage on 120 Volt.. But we are running from batteries from 12 volts to the inverter.. Therefore we take our total (example 200AH), multiply by 10 ( as 12 goes into 120 10 times). Therefore the 200AH comes to 2000AH from the batteries.
From your 12 volt appliances or items, just add up the AH used and add that to the battery needed.. Example if we need 300AH for the 12 volt items. Then add that to your 120 now converted to 12 such as the 2000Ah .. Totalling 300 plus the 2000=2300 ah..

## Slide 4: How many batteries?
If we need 2300 AH, then consider 30% of your battery being used as more than that can harm the battery.. Therefore, a 100 ah battery will give you 30 ah….
Since we need 2300 AH we divide the 2300 by 30 and get 77 batteries.
We are talking lead acid batteries.

## Slide 5: How many PV panels?
Since we figure 77 batteries.. Consider , then consider minimum 2 amp per battery to charge them as 1 amp is only a maintaining current… so 77 times 2 amp=154 amp needed..
Lets say we are using 300 watt panels, then calculate by ohms law
300 devided by 12 volt=25 amp , therefore if we need 154 amp, then simply divide 154 by 25= 6.16 panels to supply the current needed to keep your batteries charged minimum for one day’s use.

## Slide 6: Things to know
PV panels cannot be calculated properly by ohms law as they are semi conductors, you must find the label on the back of the panel.. Example if a 100 watt pv panel is used,,, then ohms law dictates that we can deliver 8 amp ( roughly) but in real life, we read the lable and it says 6.6 roughly, available ( depending the type of panel) and we must consider where the panels are located from the equator.
As for the inverter? Also consider the fact that a 1000 watt inverter will give you 8.3 amp from the inverter on 120 volts but from the battery will take 83 amp ( times 10 factor).. Plus the fact that there are losses to be considered to actually run the electronics of the inverter.

## Slide 7: summary
This presentation is very quick and rough outline on how to do the calculations.., do not be confused by AH which is for Battery and wattage which we need for the inverter , please consider that all items may run at the same time, therefore if our calculations are 4800 watt needed, then we need a minimum of 5000 watt inverter or more, but more will use more phantom power.
Consider the voltage, the wattage, the amperage and the Amp per hr.
Use a column chart to keep you organized.