## Slide 1: Lab using outdoor lighting
Sun’s photons at work

## Slide 2: We are using a 230 watt 24 volt panel

## Slide 3: Labels on the back of each Panel tells the story

## Slide 4: On this day Aug 1 2021 the skys are ready to open up to rain

## Slide 5: The solar power meter is reading 126.8 watts per sq. M

## Slide 6: Seasonal sun

## Slide 7: The outdoor temp. is about 18 degree C

## Slide 8: Angular changes through the seasons

## Slide 9: The open circuit voltage reads 33.26 volts DC

## Slide 10: The short cct current is only 1 amp

## Slide 11: The label says Isc which is current short circuit should be 8.37 A in max light

## Slide 12: Aug 2 7:30am 15 degree

## Slide 13: Sun not quite there yet

## Slide 14: 17.2 w/sq.M

## Slide 17: 8:30 am

## Slide 18: No real sun at work

## Slide 19: Nothing really on panel yet

## Slide 20: Slowly getting there

## Slide 23: 9:40

## Slide 28: 11 am

## Slide 54: Quick rinse with water

## Slide 56: For the next few hours, it will be shaded
The foliage will be blocking the light for most of the afternoon until about 4 or so. When an
Angled sun will be available for another few hours…
This one panel charges my battery bank of about 80 AH and supplies enough power to control some lighting in my kitchen and back hall as well as emergency lighting if needed.

## Slide 57: In the winter, I get more of a solar window
The solar window is the amount of sunlight hitting the panel during the day, the reason why I get more of a solar window is because there are no leaves on the trees….
the cleaner the panels, the more wattage it can produce and the better the angle, the more it can produce… this panel is not set for 30 degree, it is about 20 degree.. I do not change that because I use it to protect a device from t he weather…